## Slide 1
Final Presentation
EIN6510 - Principles of Manufacturing Systems Engineering
Team 2 - G²
Chenchu Sakthi Charan Kondugari, Chad Tucker, Samrudh U P, Chenyu Yang

## Slide 2: Product Prototype

## Slide 3: Market of Glue Gun
The Global Glue Gun market grows rapidly, especially under the COVID-19 outbreak.
Innovation of technology, safety, and variety of glue gun led to more application scenarios.
The explosive growth of users’ demand greatly enriches the application scenarios of glue gun.

## Slide 4: Customer Survey
Questions include:
  How often do you routinely make crafts as a hobby or fun?
  How important is it if the product (glue gun) is easy to control?
  How important is it if the product has a long battery life?
  How important is it if the product is light weight?
  ……

## Slide 5
Result Summary

## Slide 6: House of Quality
Rank | Engineering Requirements
1 | Number of Components
2 | One button to dispense glue stick
3 | Modular and able to glue small areas
Accessibility
Reliability
Safety
Service

## Slide 7: Product Specifications
Compact size, less components
Lightweight
Long battery life
Insulation outershell
Plastic and metal combination for the body with a rubber grip
Modular and removeable parts
Easy to clean
Size of glue sticks used should be in the normal standard
Supports different sizes of nozzles for varying glue dispense

## Slide 8: Metrics and Target Values
Compact size, less components
Lightweight
Battery life
Insulation outershell
Plastic and metal combination for the body with a rubber grip
Modular and removeable parts
Size of glue sticks used should be in the normal standard
150 x 130 x 40 (mm)
< 200 g
> 3 hours
ABS plastics as raw material
Standard size of glue gripper

## Slide 9: Architectual and Detailed Product Design

## Slide 10: Product Schematic
Drive spring
Spring
Release

## Slide 11: Specifications of Components
Internal
  Circuit board – provided by suppliers; support energy transformation
  Coupler – provided by suppliers; support energy transformation
  Spring steel – provided by suppliers; durable and flexible
  Linkage – durable
  Gripper – strong
External
  Tip – withstand high temperature (>M.P. of glue)
  Trigger – durable
  Outer shell – strong

## Slide 12: CAD Drawings
Glue tip which controls flow rate of glue out of the device
Centered Mounted Trigger
Child Lock Mechanism
Inbuilt battery Pack
Accepts standard size glue sticks

## Slide 13: CAD Drawings

## Slide 14: CAD Drawings
Gripper
Trigger
Tip
Safety Lock

## Slide 15: CAD Drawings

## Slide 16: CAD Drawings

## Slide 17: COTS PARTS
Wiring from the Battery to the Heater
Battery
Compression Spring
Coupler
Heater

## Slide 18: Bill of Materials
Part | Material | Commercial-off-the-shelf (COTS) | Manufactured | Part number
Tip | 6061 Aluminum | Yes |  | 
Trigger | ABS Plastic |  | Yes | 
Linkage | ABS Plastic |  | Yes | 
Gripper | ABS Plastic |  | Yes | 
Coupler | Galvanized steel | Yes |  | Mcmaster Part Number 7903N138
Child Lock | Carbon steel |  | Yes | 
Right side shell | ABS Plastic |  | Yes | 
Left side shell | ABS Plastic |  | Yes | 
Spring | Spring steel | Yes |  | Mcmaster Part Number 5108N003
Heater | Steel | Yes |  | 

## Slide 19: Make/Buy Analysis
Part | Material | Commercial-off-the-shelf (COTS) | Manufactured | Cost of the material (per lb.) | No of unites produced per lb. | Wastage per lb. | Material cost per unit
Trigger | ABS Plastic |  | Yes | $1.50 | 20 | 10% | $0.08
Linkage | ABS Plastic |  | Yes | $1.50 | 40 | 10% | $0.04
Gripper | ABS Plastic |  | Yes | $1.50 | 12 | 10% | $0.14
Right side shell | ABS Plastic |  | Yes | $1.50 | 8 | 25% | $0.47
Left side shell | ABS Plastic |  | Yes | $1.50 | 8 | 25% | $0.47
Glue gripper | ABS Plastic |  | Yes | $1.50 | 15 | 15% | $0.12
Spring | Spring steel | Yes |  |  |  |  | $2.38
Battery | Lithium-ion type | Yes |  |  |  |  | $4.50
Heater | Steel | Yes |  |  |  |  | $2.34
Coupler | Galvanized steel | Yes |  |  |  |  | $0.24
 |  |  |  |  |  | Total | $10.77

## Slide 20: Make/Buy Analysis
Cost of Mold | Life of mold (#of presses) | Number of cavities | Cost of mold per part | Number of parts manufactured in one hour | Direct labor cost on each part
$3,000.00 | 125,000 | 4 | $0.02 | 200 | $0.06
$3,000.00 | 120,000 | 4 | $0.03 | 250 | $0.05
$5,500.00 | 125,000 | 3 | $0.04 | 200 | $0.06
$9,000.00 | 120,000 | 2 | $0.08 | 100 | $0.13
 |  | 2 |  | 100 | $0.12
$3,600.00 | 125,000 | 4 | $0.03 | 250 | $0.05
Total $24,100.00 | 615,000 |  | $0.20 |  | $0.48

## Slide 21: Make/Buy decisions
Cost per unit = Material cost + Direct labor cost + indirect labor cost
Estimating the indirect cost = Fringe benefits + indirect labor cost
Fringe benefits = 44% of direct labor cost.
Indirect cost = 120% of direct labor cost.

## Slide 22: Make/ buy decision
Total labor cost per unit = Direct labor cost + indirect costs = 2.64 * Direct labor cost = 2.64*0.48= $1.27
Total post of production (in house)= Material cost + Labor cost = 10.77 + 1.27 = $12.03
Total Cost = 12.03 * 50,000 = $601,500
Proposed cost for manufacturing ABS plastic components by T&A = 2.62 * 50,000 = $131,000
Total Cost = 131,000 + COTS parts =131,000 + (9.46 * 50,000) = $604,000
Therefore, we have decided to manufacture the ABS plastic components in house.

## Slide 23
Process Design

## Slide 24: 2. Machines for Manufacturing
In-house Processes
  Manufacturing plastic components
    ABS
    Injection Molding Machine
  Assembly line
    Conveyor Belt

## Slide 25: Injection Molding Machine
An injection molding machine is a machine for manufacturing plastic products by the injection molding process.
Plastic injection molding is a manufacturing process for producing parts by injecting molten material (thermoplastic and thermosetting polymers) into a mold. Material for the part is fed into a heated barrel, mixed, and injected into a mold cavity, where it cools and hardens to the configuration of the cavity.
Injection molding is widely used for manufacturing a variety of parts, from the smallest components to entire body panels of cars.

## Slide 26
PART | MATERIAL | AMOUNT (lb) | LIFE OF MOLD (# of pressing) | # of cavities
Trigger | ABS plastic | 0.03 | 125,000 | 4
Linkage | ABS plastic | 0.03 | 120,000 | 4
Right side shell | ABS plastic | 0.17 | 120,000 | 2
Left side shell | ABS plastic | 0.15 | / | /
Gripper | ABS plastic | 0.05 | 125,000 | 3
Glue gripper | ABS plastic | 0.01 | 125,000 | 4
https://injection-machine.en.made-in-china.com/product/vKoJUGHAIQfh/China-Ax90-High-Precision-Plastic-Injection-Molding-Machine.html
Model | Capacity
AX-90B | 97g/s
Part | # of units produced per lb. | Wastage per lb. | # of parts manufactured in one hour
Trigger | 20 | 10% | 200
Linkage | 40 | 10% | 250
Right side shell | 8 | 25% | 100
Left side shell | 8 | 25% | 100
Gripper | 12 | 10% | 200
Glue gripper | 15 | 15% | 250

## Slide 27
YR 1 & YR 2: (50,000 units)
Trigger: 278 hours; 13,889 pressing
Linkage: 223 hours; 13,889 pressing
Side Shells (Right & Left): 667 hours; 66,667 pressing
Gripper: 278 hours; 18,519 pressing
Glue Gripper: 236 hours; 14,706 pressing
YR 3 & YR 4: (60,000 units)
Trigger: 334 hours; 16,667 pressing
Linkage: 267 hours; 16,667 pressing
Side Shells (Right & Left): 800 hours; 80,000 pressing
Gripper: 334 hours; 22,223 pressing
Glue Gripper: 283 hours; 17,647 pressing
YR 5: (70,000 units)
Trigger: 389 hours; 19,445 pressing
Linkage: 312 hours; 19,445 pressing
Side Shells (Right & Left): 934 hours; 93,334 pressing
Gripper: 389 hours; 25,927 pressing
Glue Gripper: 330 hours; 20,589 pressing
Summary of Manufactured Plastic Components
3 Injection Molding Machines

## Slide 28
Process Flow chart

## Slide 29
Task | Process | Task time(min)
1 | Take parts to assembly area | 0.3
2 | Assemble heater into side shell | 0.5
3 | Assembled linkage, trigger | 0.4
4 | Assembled glue gripper | 0.4
5 | Assembled tip | 0.3
6 | Assembled other side shell | 0.7
7 | Insert battery | 0.5
8 | Quality Control | 2
Total time |  | 5.1
Task time
IDEAL CYCLE TIME:
A total of 195 units is required per day. Factory will operate 1 shift per day at 90% efficiency. 195 units per shift.
Productive hours per shift= 8 hours per shift x 0.93efficiency = 7.44hour per shift
Desired Cycle time= 7.44 x 60/195= 2.289min, For 4 workers= 2.289 x 4= 9.156min

## Slide 30
Task number | Immediate predecessor | Task time
1 | - | 0.3
2 | 1 | 0.5
3 | 2 | 0.4
4 | 2 | 0.4
5 | 3 | 0.3
6 | 4,5 | 0.7
7 | 6 | 0.5
Precedence Table

## Slide 31
Assembly line Precedence Diagram

## Slide 32
Facility Design

## Slide 33
Facility
4750 NW US 441, Gainesville, FL 32609
7480 sq.ft

## Slide 34
Plant Layout

## Slide 35
Process | Equipment | Number | Dimensions ft | Area per unit Sq. ft | Total process area sq. ft
Lathe | CNC lathe | 1 | 5x2 | 10 | 10
Molding | Ax90 | 3 | 11.7x4.1 | 50 | 150
Bend | Bar bending machine | 1 | 3x3 | 9 | 9
Assembly |  | 1 | 30x40 | 1200 | 1200
Packaging |  | 1 | 20x40 | 800 | 800
 |  |  |  | Total | 1449
 |  |  |  | 50% aisles space | 991.1
 |  |  |  | Total area for production and assembly | 2173.5
Production Areas:

## Slide 36
Activity | Area sq. ft
Raw material Storage | 350
Finished good storage | 600
Office | 1250
Locker rooms | 270
Maintenance | 160
Tool crib | 160
Shipping and receiving | 600
Showroom | 1080
Restroom | 100
Total space required | 4570
Non-production areas:
Total area needed: 2173.5+4570 = 6743.5sq.ft

## Slide 37
Floor Plan

## Slide 38: Economic Analysis

## Slide 39: Overall Initial Capital Investments
Labor Rate for four months |  |  | 
Role | Quantity | Price per person | Total
Technician | 4 | $13,325 | $53,300
Office Manager | 1 | $13,750 | $13,750
Office Assistant | 1 | $11,675 | $11,675
Engineer | 1 | $26,600 | $26,600
 |  | Total | $105,325

## Slide 40: Overall Initial Capital Investment
Property Expenses |  |  |  | 
 | Size sqft | Price per sqft | Price per month | Total
Office/Warehouse Space for lease | 7480 | $0.58 | $4,338 | $17,353
Utility cost | 7480 | $2.10 | $15,708 | $62,832
Property/Liability Insurance |  |  | $80 | $320
Building Maintenance |  |  | $150 | $600
 |  | Total | $20,276 | $81,105

## Slide 41: Overall Initial Capital Investment
Raw Material Costs | Quantity for 4 months | price per unit | Total
Abs Plastic | 10,000lbs | 1.5lb | $15,000
Aluminum 6061 T6 rod | 695 12" rods | 9.15 per foot | $6,359
Steel rod | 5,334 12" rods | 1.53 per foot | $8,161
COTS Costs | Quantity for 4 months | price per unit | Total
Spring | 16,667 | $2.38 | $39,667
Coupler | 16,667 | $1.30 | $21,667
Glue Gun heating element | 16,667 | $4.00 | $66,668
 |  | Total | $128,002

## Slide 42: Overall Initial Capital Investment
Inventory= Amount needed for production + desired end inventory
Inventory |  |  |  | 
 | Amount needed for four months | Desired end inventory | Total Inventory | Total Price
Gripper | 16,667 | 7,333 | 24,000 | $21,600
Glue Gripper | 16,667 | 7,333 | 24,000 | 
Trigger | 16,667 | 7,333 | 24,000 | 
Linkage | 16,667 | 7,333 | 24,000 | 
Right Side Shell | 16,667 | 7,333 | 24,000 | 
Left Side Shell | 16,667 | 7,333 | 24,000 | 
Tip | 16,667 | 7,333 | 24,000 | $9,150
Child Lock | 16,667 | 7,333 | 24,000 | $11,751
Spring | 16,667 | 7,333 | 24,000 | $57,120
Coupler | 16,667 | 7,333 | 24,000 | $31,200
Glue Gun Heating Element | 16,667 | 7,333 | 24,000 | $96,000
 |  |  | Total | $226,821

## Slide 43: Overall Initial Capital Investment
Overall Investment for four months | Cost
Labor Rate | $105,325
Rent/Utilities | $81,105
Raw Materials | $42,501
COTS Parts | $184,320
Cost of Machinery | $65,000
Total Investment Cost | $478,251

## Slide 44: Sales forecast and Margins
Year | Forecasted sales | Direct labor cost | Property expenses | Raw material cost | Cost of machinery | Total Investment | Gross margin | Net Margin | Total revenue
Year 1 | 50,000 | $421,300.00 | $243,312.00 | $384,006.00 | $65,000.00 | $1,113,618.00 | $828,700.00 | $136,382.00 | $1,250,000.00
Year 2 | 50,000 | $421,300.00 | $243,312.00 | $384,006.00 |  | $1,048,618.00 | $828,700.00 | $201,382.00 | $1,250,000.00
Year 3 | 60,000 | $505,560.00 | $243,312.00 | $460,807.00 |  | $1,209,679.00 | $994,440.00 | $290,321.00 | $1,500,000.00
Year 4 | 60,000 | $505,560.00 | $243,312.00 | $460,807.00 |  | $1,209,679.00 | $994,440.00 | $290,321.00 | $1,500,000.00
Year 5 | 70,000 | $589,820.00 | $243,312.00 | $537,608.00 |  | $1,370,740.00 | $1,160,180.00 | $379,260.00 | $1,750,000.00

## Slide 45: Estimated Profit
Year | Sales | Net Margin | Tax(@37%) | Profit
Year 1 | 50,000 | $136,382.00 | $50,461.34 | $85,920.66
Year 2 | 50,000 | $201,382.00 | $74,511.34 | $126,870.66
Year 3 | 60,000 | $290,321.00 | $107,418.77 | $182,902.23
Year 4 | 60,000 | $290,321.00 | $107,418.77 | $182,902.23
Year 5 | 70,000 | $379,260.00 | $140,326.20 | $238,933.80

## Slide 46: Estimated working capital
Working Capital = Cost of Goods Sold (Estimated) * (No. of Days of Operating Cycle / 365 Days) + Bank and Cash Balance
Working capital = $1,250,000*(300(excluding holidays)/365)+$250,000=$1,277,397.26

## Slide 47: THANK YOU! Q&A